## Slide 1
T1_9 Turbine Hub --- Overview
T1_9 turbine hub: cylindrical surface at constant radius
Input: T1_9_hub_raw.stl (raw triangulated surface)
Goal: extract quadrilateral block structure for CFD meshing
arrow
arrow
arrow
arrow
arrow

## Slide 2
Unwrapped Hub Surface --- Cylindrical Mapping
Isometric mapping: distortion-free, preserves triangulation
Domain becomes rectangular with a blade-shaped hole
Periodic $\theta$-boundaries (pitch = $\pi/4$ for 8 blades)
\theta = \arctan(\frac{y}{x}), s = r \cdot \theta, t = z
\theta

## Slide 3
Boundary Crosses --- 4-RoSy Cross-Field
4-RoSy field: invariant under $90^\circ$ rotation
Representative vector encodes direction modulo $\pi/2$
Boundary-aligned via Dirichlet conditions
\mathbf{c}(x) = (\cos 4\theta(x), \sin 4\theta(x))
90^\circ

## Slide 4
Cross-Field $arrow$ Representative Vector
Each cross has 4 symmetric representatives (rotated by $\pi/2$)
Pick the one closest to the desired direction
Enables streamline integration along smooth field lines
\mathbf{v}(x) = \arg\max_{\mathbf{c} \in cross(x)} \langle \mathbf{c}, \mathbf{d}(x) \rangle
\mathbf{d}(x)
Citation: Kn\"{o}ppel et al., "Globally optimal direction fields," SIGGRAPH 2013.

## Slide 5
Frame Field --- Harmonic Laplace + Dirichlet
Solve harmonic Laplace for a smooth angle field inside the domain
Dirichlet BC: boundary values align with wall cross-vectors (4-RoSy)
Normalize to extract the 4-RoSy representative ($\mod \pi/2$)
\Delta \theta = 0 s.t. \theta|_{\partial\Omega} = \theta_{wall}
\mod \pi/2
Citation: } Kn\"{o}ppel et al., "Globally optimal direction fields", SIGGRAPH 2013

## Slide 6
Singularities --- Index & Poincar\'{e
4 tip singularities, each with index $-\tfrac{1}{4}$
Poincar\'{e-Hopf:} sum of indices equals Euler characteristic $\chi$
Periodic cylinder: $\chi = 0$, so indices must balance
index(p) = \frac{1}{2\pi} \oint_{\partial B(p)} d\theta
\sum_i index(p_i) = \chi(\Omega)
-\tfrac{1}{4}
\chi = 0
Citation: } Kowalski 2015, ``Blocking piecewise-linear domains''

## Slide 7
Streamline Integration --- Runge-Kutta-Heun
Integrate along representative vectors emanating from singularities
RK-Heun: 2nd-order accurate, stable near singularities
Terminate on boundary, singularity, or $c_0$ corner
\mathbf{p}_{n+1} = \mathbf{p}_n + \frac{1}{2}(\mathbf{k}_1 + \mathbf{k}_2)
Citation: } Kowalski 2015, ``Blocking piecewise-linear domains'' (Prop.~9)

## Slide 8
Streamline Simplification --- Merging & Splitting
Merge nearby streamlines at singularities (angle criterion)
Split at transversal crossings (T-junctions)
Result: clean quad-only block boundaries
120^\circ \le \alpha \le 240^\circ (3-valent), 144^\circ \le \alpha \le 216^\circ (5-valent)
\gamma_{12}(s) = (1-s)\gamma_1(s) + s\gamma_2(s)
Citation: } Xiao et al.~2020, ``Robust topology decomposition of 2D domains'' (Alg.~2)

## Slide 9
Postprocessing --- Periodic Boundary Closure
Collapse 3-sided seam wedges (Xiao-style simplification)
Master-slave seam conformity (DLR Sauer/Morsbach 2023 sec 2.7)
Result: periodic block structure with conforming seam
Citation: } Sauer/Morsbach 2023, ``Automated blocking for turbomachinery'', sec 2.7

## Slide 10
Transfinite Interpolation --- Coons Patch
Bilinear interpolation from 4 boundary curves
Guarantees $C^0$ continuity at block edges
Cell counts solved conforming: opposite sides match
Citation: } Coons 1967, ``Surfaces for Computer-Aided Design''

## Slide 11
Periodic Boundaries --- 3$\times$ Tiled Passages
3 passages tiled: shifts $-pitch$, $0$, $+pitch$
Interior seams: grid points of neighboring copies coincide (CFD-conforming)
Visual check: master-slave conformity confirmed by overlay
-pitch
+pitch
Citation: } DLR Sauer/Morsbach 2023, sec 2.7 master-slave